## Slide 1: Digital Logic
Dr. Charles R. Severance
www.ca4e.com
online.dr-chuck.com

## Slide 2: Outline
What is Computer Architecture
What is a Central Processing Unit (CPU)
Start with gates - AND / OR / NOT / XOR …
Adding numbers with gates – half and full adders
Number representation – Base 2 and Base 10 (hexadecimal)
Storing data with gates – Latches and Flip-Flops

## Slide 3: Computer Architecture
Within the computer data is moved using electric wires
Each wire generally has a voltage that is either a "0" or "1"
Wires connect components like the CPU, Memory, or other devices
https://en.wikipedia.org/wiki/Printed_circuit_board
A sound chip from a 1980's
Commodore 64 connected to the
motherboard

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
From: Python for Everybody (www.py4e.com)

## Slide 5: Definitions
Central Processing Unit: Runs the Program - The CPU is always wondering “what to do next”. Not the brains exactly - very dumb but very very fast
Input Devices: Keyboard, Mouse, Touch Screen
Output Devices: Screen, Speakers, Printer, DVD Burner
Main Memory: Fast small temporary storage - lost on reboot - aka RAM
Secondary Memory: Slower large permanent storage - lasts until deleted - disk drive / memory stick
What
Next?

## Slide 6
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
if x< 3: print
From: Python for Everybody (www.py4e.com)
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 7
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 8: Building Microprocessors

## Slide 9: Very Large Scale Integration
We went from 16 transistors on a board 4 inches on a side to billions of transistors in a chip 0.5 inches on a side

## Slide 10: CPU Design Process
We start with gates and build reusable components and then combine those components to implement programmable digital logic
Software translates our abstract design into transistors and then creates an optimal layout for our chip
Photo lithography is then used to build the chip

## Slide 11: Adding numbers with gates
Gates are now our low-level building blocks – we can combine them to solve problems

## Slide 12: Classic Mathematical Logic Gates
A | Q
0 | 1
1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Not
And
Or
Exclusive Or
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 13: Representing Numbers with 0's and 1's
If we are going to do significant computations, we will need a way to represent numbers as electrical values
"Normal" numbers are Base-10
We know the place values of Base-10 numbers
To manipulate numbers with gates, we use Base-2 numbers
Base-10
12310 = 1 x 102 + 2 x 101 + 3 * 100
= 1 x 100 + 2 * 10 + 3 * 1 = 12310
Base-2
1102 = 1 * 22 + 1 * 21 + 0*20 =
= 4 + 2 + 0 = 610

## Slide 14: Keep it simple for now
Base–2 to Base-10 for numbers less than 8
A.k.a. 3-bit numbers
Base-10 | Base-2
0 | 0
1 | 1
2 | 10
3 | 11
4 | 100
5 | 101
6 | 110
7 | 111
1 1 0 = 6
4s 2s 1s

## Slide 15: Nixie Tubes – Binary to Decimal Display
1 1 0 = 6
4 2 1
https://en.wikipedia.org/wiki/Nixie_tube

## Slide 16
https://www.ca4e.com/tools/nixie/

## Slide 17: Base-2 Math
1 (1)
+ 1 (1)
1 0 (2)
1 0 (2)
+ 1 0 (2)
1 0 0 (4)
1 0 0 (4)
+ 1 0 0 (4)
1 0 0 0 (8)
1 1 (3)
+ 1 (1)
1 0 0 (4)
1 1 (3)
+ 1 0 (2)
1 0 1 (5)
1 1 1 (7)
+ 1 (1)
1 0 0 0 (8)

## Slide 18: Half Adder
Compute the sum of two base-2 digits and produce a sum and carry.
HALF
Adder
A
B
SUM
Carry
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 19: Half Adder
Compute the sum of two base-2 digits and produce a sum and carry.
HALF
Adder
A
B
SUM
Carry
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 20: Full Adder
Adds three 0/1 numbers for a sum/carry between 0 and 3
Carry in | A | B | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
1 (CIN)
1 (A)
+ 1 (B)
1 1 (3)
FULL
Adder
A
B
SUM
Carry out
Carry In

## Slide 21: Full Adder
Adds three 0/1 numbers for a sum/carry between 0 and 3
1 (CIN)
0 (A)
+ 1 (B)
1 0 (2)
Notes: A diagram of a full adder circuit with inputs A and B with a Carry-In of CIN. The output is single bit SUM and a single but Carry Out. The circuit consisted of two half adders connected and an OR gate to compute the carry out when all the inputs are 1.

## Slide 22: Chaining full adders
0 1 0 (2)
+ 1 0 1 (5)
1 1 1 (7)

## Slide 23: Three Bit Adder Component
Once we know how to make something, add a component to our design system
0 1 0 (2)
+ 1 0 1 (5)
1 1 1 (7)

## Slide 24: Storing data with gates
Latches and Flip-Flops

## Slide 25: Storing Data Using Feedback Loops
The simplest latch is a "Set-Reset" latch using two NOR gates
The output of each NOR gate is connected to the one of the inputs of the other NOR gate
https://en.wikipedia.org/wiki/Flip-flop_%28electronics%29
A | B | NOR
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
S | R | Q
0 | 0 | Maintain
0 | 1 | 0
1 | 0 | 1
1 | 1 | ???

## Slide 26: SR Flip-Flop / Latch
When S and R are zero, the latch maintains its value
When S=0 and R=1 the internal value becomes 0
When S=1 and R=0 the internal value becomes 0
Setting both to 1 means output is undefined
S | R | Q
0 | 0 | Maintain
0 | 1 | 0
1 | 0 | 1
1 | 1 | ???

## Slide 27: SR Flip-Flop / Latch
S | R | Q
0 | 0 | Maintain
0 | 1 | 0
1 | 0 | 1
1 | 1 | ???
Set / Reset
Stored Value

## Slide 28: My Simulators Can't Build an SR Latch :(
My Digital Logic Builder does not handle feedback loops so you can't build a SR latch from two NOR gates (unless I fix it)
SR Circuit Fails 
SR Component Works

## Slide 29: Gated D Latch
The Gated D Latch has a D (data) and a C (clock) inputs.
If C is zero, D is ignored, and the output is the most recent stored value
If C is 1, D is copied into the internal state
C | D | Q
0 | 0 | Maintain
0 | 1 | Maintain
1 | 0 | 0
1 | 1 | 1
C

## Slide 30: Gated D Latch
Store 1
Store 0
Ignore D
Ignore D
Clock to 0
Clock to 0

## Slide 31: Stack D Latches to Make a 3-bit Register

## Slide 32: Summary
In this lecture we started with simple gates like AND and OR
We built latches / registers for storage

## Slide 33: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here